## Slide 1: Voronica MCU Configuration
Manta M8P V1.0

## Slide 2
X
X
Y
E
X-Stop
X
Y
Z
TAP
Z0
Z1
Z2
Z3
Y-Stop
Z-Stop
Tap (z)
TH0
THB
NEO Pixels
RGB1
TH-SB
CASE
TH-HE
TH-part

## Slide 3: Steppers / Drivers General Info
Parts source: West3D
  V2.4 LDO Motor Kit
  BTT TMC2226 Driver (x7)
Motors
  E – Axis (1x) StealthBurner CW2 mod
    LDO-36STH20-1004AHG(XH)
      NEMA14 36mm pancake motor
  X – Y Axis (2x)
    LDO-42STH48-2004MAH(VRN)
  Z – Axis (4x)
    LDO-42STH48-2004AC(VRN)
Stepper Drivers
  BTT TMC2226 v1.0
    interface: UART
    equivalent to: TMC2209
    TMC2226 Trinamic Datasheet

## Slide 4: E-Axis Config
MCU Motor Pin header: 3A (3B not used)

## Slide 5: End Stops
X – Axis
  pin: PF3
Y – Axis
  pin: PF4
Z – Axis (DO NOT USE)
  Added end-stop but don’t need b/c using the ”Voron Tap”
  pin: PF5
Voron Tap (Z-Axis)
  pin: PC0

## Slide 6: Klipper Configuration
Follow these guides to get the printer.cfg setup:
  Voron 2.4 docs – Mini12864 LCD Display Klipper wiring and config
  Voron 2.4 docs – Software Configuration
  Voron-Tap Klipper configuration
Mods and config varients
  Klipper NeoPixel Templates
  Obico – Klipper Camera
Calibration procedures to run
  HotEnd/Toolhead: PID_CALIBRATE
  Voron-tap:
    PROBE_CALIBRATE
      TIP: Before calibrating, switch to the spray coated spring steel sheet side
      need to manually calibrate the probe’s Z offset
    probe_accuracy samples=100
      Heat soak the machine and then run a bunch of times
      See 7. Voron-Tap Post-Install Setup
  Quad gantry leveling: QUAD_GANTRY_LEVEL

## Slide 7: Voron-Tap Post-Install Setup
Update your printer.cfg as recommended in Tap Klipper Instructions
Home Z and test virtual Z endstop by lifting tool-head
Heat soak your machine and run a couple probe_accuracy samples=100 to "break-in" your probe
Run a few more probe_accuracy checks (default of 10 probes)
For well-built machines you can expect to see between 0.0000 and 0.0008 standard deviation.

## Slide 8: Heat Soaking
Forum posts
  How are you determining heat-soak duration, and for how long?

## Slide 9: Links
BTT Manta M8P Resources
BTT TMC 2226 Stepper drive datasheet
  Other:
    TMC2209 Pin Out (FYSETC)
BTT TMC 2209 Datasheet
TMC2226 Datasheet
Keenovo build plate heating mat
  Hotbed thermistor NTC 100k datasheet
  R-T Table Sheet
VoronTap Klipper configuration guide
Klipper Rotation Distance Calculator

## Slide 10: Backup / Scratch starts here
2/19/23

## Slide 12: https://forum.vorondesign.com/threads/manta-m8p-diagrams-for-trident-and-v2-4.48/

## Slide 13: https://forum.vorondesign.com/threads/manta-m8p-diagrams-for-trident-and-v2-4.48/